## Slide 1: Unit – 1
Introduction to number systems and logic gates

## Slide 2
Number systems – binary, decimal, octal, hexadecimal; codes – grey, BCD, excess – 3, ASCII, parity, binary arithmetic – addition, subtraction, multiplication, division using sign magnitude, 1’s complement, 2’s complement, BCD arithmetic, logic gates – AND, OR, NOT, NAND, NOR, EX-OR, EX-NOR

## Slide 3: Computer architecture
Attributes of a system visible to a programmer/those attributes that have a direct impact on the logical execution of a program.
Attributes:
  Instruction set.
  No. of bits to represent various data types.
  I/O mechanisms.
  Techniques for addressing memory.

## Slide 4: Computer
Complex systems.
Millions of elementary electronic components.
Fast electronic calculating machine, accepts digitized input information, process the internally stored instructions and produces result.

## Slide 5: Computer
Computer program – list of instructions.
Memory – internal storage.
Personal computer – common type.
Notebook computers – a compact version of the personal computer with all of the components packed into a single unit.
Workstations – high resolution graphics, input or output
  Retains the resolution of desktop computers.
  More computational power.
  Used in engineering applications.

## Slide 6: Computer
Servers – sizable database storage units.
  Handles large volumes of request to access the data.
Super computer – used for large scale numerical calculations.

## Slide 7: Functional unit
5 independent parts:
  Input
  Memory
  ALU
  Output
  Control units

## Slide 8
Input
Output
Input / Output
ALU
Control
Processor
Memory

## Slide 9
Instructions/machine instructions:
  Explicit commands that,
    Govern the transfer information within the computer as well as between computer and its I/O devices.
    Specify the arithmetic and logic operations to be performed.
    Program list of instructions that perform a task.
    Data: number and encoded characters used as operands.
    Compiler: task of compiling high level source program into machine instructions.
    Bits: binary digits
      ON/OFF – 1/0

## Slide 10: Number systems
To express/represent numbers.
Decimal number system is the most commonly used – base 10.
Number systems in computer include,
  Binary – base 2
  Octal – base 8
  Hexadecimal – base 16

## Slide 12: Decimal number system
Base – 10
It represents numeric value with 10 digits.
Any number to decimal conversion:
  Multiply each digit by its own base power the position.

## Slide 13: Binary to decimal conversion
  Multiply each digit by 2^n, where n is the position.

## Slide 14: Binary to decimal conversion
  Fractional conversion

## Slide 15: Octal to decimal conversion

## Slide 16: Hexadecimal to decimal conversion

## Slide 17: Hexadecimal to binary conversion
Convert each hexadecimal digit to its equivalent binary.

## Slide 18: Octal to binary conversion
Convert each digit to its equivalent 3 bit binary.

## Slide 19: Decimal to binary conversion
Divide the number by 2, keep track of the reminder.

## Slide 20: Decimal to binary conversion
Divide the number by 2, keep track of the reminder.

## Slide 21: Octal to hexadecimal conversion
Octal - > binary -> hexadecimal

## Slide 22: Memory size

## Slide 23: Codes
Gray code:
  Used to reduce the occurrence of errors.
  Only one bit is changed at a time.

## Slide 24: Codes (Gray code)
Decimal Number | Binary Number | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000

## Slide 25: Binary coded decimal
Coding is done in 8 – bit / 4 – bit.

## Slide 26: Excess – 3 code
Overcomes the deficiency in BCD code.
Decimal Digit | BCD Code | Excess-3 Code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 27: Excess – 3 code
31
Digit | BCD
3 | 0011
1 | 0001
Decimal | BCD | Excess-3
3 | 0011+0011 | 0110
1 | 0001+0011 | 0100

## Slide 28: Excess – 3 code
81.61
So, the excess-3 code of the decimal number 81.61 is 1011 0100.1001 0100
Digit | BCD
8 | 1000
1 | 0001
6 | 0110
1 | 0001
Decimal | BCD | Excess-3
8 | 1000+0011 | 1011
1 | 0001+0011 | 0100
6 | 0110+0011 | 1001

## Slide 29: Excess – 3 code
81.61
So, the excess-3 code of the decimal number 81.61 is 1011 0100.1001 0100
Digit | BCD
8 | 1000
1 | 0001
6 | 0110
1 | 0001
Decimal | BCD | Excess-3
8 | 1000+0011 | 1011
1 | 0001+0011 | 0100
6 | 0110+0011 | 1001

## Slide 30: ASCII code
ASCII – American Standard Code for Information Interchange.
Standard character set for computers and electronic devices, developed in 1960s.
Contains 128 characters.
It contains the numbers from 0-9, the upper and lower case English letters from A to Z, and some special characters.
The character sets used in modern computers, in HTML, and on the Internet, are all based on ASCII.

## Slide 31
Char | Number | Description
NUL | 00 | null character
SOH | 01 | start of header
STX | 02 | start of text
ETX | 03 | end of text
EOT | 04 | end of transmission
ENQ | 05 | enquiry
ACK | 06 | acknowledge
BEL | 07 | bell (ring)
BS | 08 | backspace
HT | 09 | horizontal tab
LF | 10 | line feed
VT | 11 | vertical tab
FF | 12 | form feed
CR | 13 | carriage return
SO | 14 | shift out
SI | 15 | shift in

## Slide 32
DLE | 16 | data link escape
DC1 | 17 | device control 1
DC2 | 18 | device control 2
DC3 | 19 | device control 3
DC4 | 20 | device control 4
NAK | 21 | negative acknowledge
SYN | 22 | synchronize
ETB | 23 | end transmission block
CAN | 24 | cancel
EM | 25 | end of medium
SUB | 26 | substitute
ESC | 27 | escape
FS | 28 | file separator
GS | 29 | group separator
RS | 30 | record separator
US | 31 | unit separator
DEL | 127 | delete (rubout)

## Slide 33
 | 32 | space
! | 33 | exclamation mark
" | 34 | quotation mark
# | 35 | number sign
$ | 36 | dollar sign
% | 37 | percent sign
& | 38 | ampersand
' | 39 | apostrophe
( | 40 | left parenthesis
) | 41 | right parenthesis
* | 42 | asterisk
+ | 43 | plus sign
, | 44 | comma
- | 45 | hyphen
. | 46 | period
/ | 47 | slash

## Slide 34
0 | 48 | digit 0
1 | 49 | digit 1Try it
2 | 50 | digit 2Try it
3 | 51 | digit 3Try it
4 | 52 | digit 4Try it
5 | 53 | digit 5Try it
6 | 54 | digit 6Try it
7 | 55 | digit 7Try it
8 | 56 | digit 8Try it
9 | 57 | digit 9Try it
: | 58 | colonTry it
; | 59 | semicolonTry it
< | 60 | less-thanTry it
= | 61 | equals-toTry it
> | 62 | greater-thanTry it
? | 63 | question markTry it
@ | 64 | at sign

## Slide 35
A | 65 | uppercase ATry it
B | 66 | uppercase BTry it
C | 67 | uppercase CTry it
D | 68 | uppercase DTry it
E | 69 | uppercase ETry it
F | 70 | uppercase FTry it
G | 71 | uppercase GTry it
H | 72 | uppercase HTry it
I | 73 | uppercase ITry it
J | 74 | uppercase J

## Slide 36
A | 65 | uppercase ATry it
B | 66 | uppercase BTry it
C | 67 | uppercase CTry it
D | 68 | uppercase DTry it
E | 69 | uppercase ETry it
F | 70 | uppercase FTry it
G | 71 | uppercase GTry it
H | 72 | uppercase HTry it
I | 73 | uppercase ITry it
J | 74 | uppercase J

## Slide 37
K | 75 | uppercase KTry it
L | 76 | uppercase LTry it
M | 77 | uppercase MTry it
N | 78 | uppercase NTry it
O | 79 | uppercase OTry it
P | 80 | uppercase PTry i
Q | 81 | uppercase QTry it
R | 82 | uppercase RTry it
S | 83 | uppercase STry it
T | 84 | uppercase TTry it
U | 85 | uppercase U

## Slide 38
V | 86 | uppercase VTry it
W | 87 | uppercase WTry it
X | 88 | uppercase XTry it
Y | 89 | uppercase YTry it
Z | 90 | uppercase ZTry it
[ | 91 | left square bracketTry it
\ | 92 | backslashTry it
] | 93 | right square bracketTry it
^ | 94 | capTry it
_ | 95 | underscore

## Slide 39
` | 96 | grave accentTry it
a | 97 | lowercase aTry it
b | 98 | lowercase bTry it
c | 99 | lowercase cTry it
d | 100 | lowercase dTry it
e | 101 | lowercase eTry it
f | 102 | lowercase fTry it
g | 103 | lowercase gTry it
h | 104 | lowercase hTry it
i | 105 | lowercase i

## Slide 40
j | 106 | lowercase jTry it
k | 107 | lowercase kTry it
l | 108 | lowercase lTry it
m | 109 | lowercase mTry it
n | 110 | lowercase nTry it
o | 111 | lowercase oTry it
p | 112 | lowercase pTry it
q | 113 | lowercase qTry it
r | 114 | lowercase rTry it
s | 115 | lowercase s

## Slide 41: Parity code
Most common way to detect errors that occur while transmitting data.
An extra bit known as parity bit is added to the original data.
On the receiving end the parity bit is checked.
The received data is accepted and forwarded to upper layers, if the parity bit is found to be correct.
2 types:
  Odd parity
  Even parity

## Slide 42: Parity code
Odd parity:
  Total number of 1s is odd.
Even parity:
  Total number of 1s is even.

## Slide 43
4-bit Binary Message | Even Parity bit (Peven) | Odd Parity bit (Podd)
0000 | 0 | 1
0001 | 1 | 0
0010 | 1 | 0
0011 | 0 | 1
0100 | 1 | 0
0101 | 0 | 1
0110 | 0 | 1
0111 | 1 | 0
1000 | 1 | 0

## Slide 44: Binary addition
Basic operation
Rules:
  0+0=0
  0+1=1
  1+0=1
  1+1=10

## Slide 45: Binary addition

## Slide 46: Binary addition

## Slide 47: Binary addition

## Slide 48: Binary addition

## Slide 49: Binary Addition

## Slide 50: Binary subtraction
Rules:

## Slide 51: Binary subtraction
1 0 1 1

## Slide 52
0 1 0 1

## Slide 53
0 0 0 0 1

## Slide 54: Binary multiplication
Rules:

## Slide 55: Binary multiplication
1 1 1 1 0

## Slide 56: Binary division
101010 / 110
110
101010
110
1001
110
0110
110
111
0

## Slide 57: Sign magnitude
Sign magnitude is represented using MSD.
If the number is positive, MSD is 0.
If the number is negative, MSD is 1.
Signed decimal | sign-magnitude
+6 | 0110
-6 | 1110
+0 | 0000
-0 | 1000
+7 | 0111
-7 | 1111

## Slide 58: 1’s complement
101010 ->
110110 - >
11100 ->

## Slide 59: 2’s complement
1’s complement + 1
101010 ->
110110 - >
11100 ->

## Slide 60
101 <- (+5) First Number
+
011 <- (+3) Second Number
1000 <- (+8) Sum

## Slide 61
1100 <- (-4) First number
+ 0010 <-(+2) Second Number
1110 <- (-2) Sum

## Slide 62: Binary addition
While adding a numbers with same sign, just add and put the same sign.
If the numbers are of different sign, subtract the big number from small one and put the sign of the big one.

## Slide 63: Binary addition using sign magnitude
Example 1:
  Add + 7 and + 4
  + 7 -> 111
  +4 -> 100
  1011
1 is left as carry
MSD is 0, so the number is positive

## Slide 64: Binary addition using sign magnitude
Example 2:
  Add -7 and - 4
  7 - > 1112
  4 -> 1002
  - 7  1’s complement of 7 + 1 -> 000+1 -> 001
  - 4  1’s complement of 4 + 1 ->011+1 -> 100
  0101
Remove the carry bit
MSD is 1, so the result is negative and take 2’s complement.

## Slide 65: Binary addition using sign magnitude
  Since MSD is 1, take 2’s complement.
  2’s complement of 0101
  -> 1010 + 1 = 01011 -> 1110

## Slide 66: Binary subtraction using sign magnitude
A-B => A + 2’S Complement of B
B-A => B + 2’s complement of A

## Slide 67
Example 1:
  Subtraction of 7 and 4
  7 -> 111 +
  2’s complement of 4 -> 100
                011 310
                * MSD=0 indicates that the resultant is positive.

## Slide 68
Example 2:
  Subtraction of 4 and 7
  4 -> 100 +
  -7 -> 001
  101
  MSD is 1, so the number is negative.
  So take 2’s complement.
  1’s complement of 101  010
  2’s complement  010+1 = 011 (310 )
  Since, MSD is 1 result is -310

## Slide 69: Binary multiplication

## Slide 70: Binary multiplication

## Slide 71: Example
1 1 0 1 1 1 1 0 1

## Slide 72: Example

## Slide 73: Logic gates
Building block of digital circuits.
Make decisions based on a combination of digital signals coming from its inputs.
Logic gates are based on Boolean algebra.
False represents 0, and true represents 1.
Seven basic logic gates: AND, OR, XOR, NOT, NAND, NOR, and XNOR.

## Slide 74: NOT gate
Also called as the inverter gate.
Has only one input.
It just inverts the input.
Input 1 | Result
1 | 0
0 | 1

## Slide 75: AND gate
If both the inputs are true, the result is true else the result is false.
Input 1 | Input 2 | Result
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0

## Slide 76: NAND gate
AND gate followed by an inverter.
The output is false if both inputs are true.
Input 1 | Input 2 | Result
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 1

## Slide 77: OR gate
If any one of the input is true, the result is true else the result is false.
Input 1 | Input 2 | Result
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 78: NOR gate
NOR gate followed by an inverter.
The output is true if both inputs are false.
Input 1 | Input 2 | Result
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1

## Slide 79: XOR gate (eXclusive OR)
If either one of the input is true, the result is true else the result is false.
If both the inputs are same, the result is false.
Input 1 | Input 2 | Result
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 80: eXclusive NOR (XNOR) gate
XOR gate followed by an inverter.
The output is true if both inputs are same.
Input 1 | Input 2 | Result
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1