## Slide 1: Unit V
Parallelism

## Slide 2: Syllabus
Need, types, applications and challenges, Architecture of Parallel Systems – Flynn’s classification; ARM Processor: The thumb instruction set, Processor and CPU cores, Instruction Encoding format, Memory load and Store instruction, Basics of I/O operations. Case study: ARM 5 and ARM 7 Architecture

## Slide 3: Parallelism
Why parallelism? – ticket counter example.
Executing two or more operations at the same time is known as parallelism.
Parallel processing is a method to improve computer system performance by executing two or more instructions simultaneously
A parallel computer is a set of processors that are able to work cooperatively to solve a computational problem.
Two or more ALUs in CPU can work concurrently to increase throughput
The system may have two or more processors operating concurrently

## Slide 4: Goals of parallelism
To increase the computational speed (ie) to reduce the amount of time that you need to wait for a problem to be solved
To increase throughput (ie) the amount of processing that can be accomplished during a given interval of time
To improve the performance of the computer for a given clock speed
To solve bigger problems that might not fit in the limited memory of a single CPU

## Slide 5: Applications of Parallelism
Numeric weather prediction
Socio economics
Finite element analysis
Artificial intelligence and automation
Genetic engineering
Weapon research and defence
Medical Applications
Remote sensing applications

## Slide 6: Types of parallelism
1. Hardware Parallelism
2. Software Parallelism

## Slide 7: Hardware Parallelism :
Objective – to increase the processing speed.
Based on the hardware architecture (2 types):
Processor parallelism and
Memory parallelism.

## Slide 8
Processor parallelism – the computer architecture has multiple nodes, multiple CPUs or multiple sockets, multiple cores, and multiple threads.
Memory parallelism – shared memory, distributed memory, hybrid distributed shared memory, multilevel pipelines, etc.
Otherwise called Parallel Random Access Machine (PRAM).
“It is an abstract model for parallel computation which assumes that all the processors operate synchronously under a single clock and are able to randomly access a large shared memory”.
In particular, a processor can execute an arithmetic, logic, or memory access operation within a single clock cycle.
Overlapping or pipelining instructions are used to achieve parallelism.

## Slide 9: Hardware Parallelism
One way to characterize the parallelism in a processor is by the number of instruction issued per machine cycle.
If a processor issues k instructions per machine cycle, then it is called a k-issue processor.
In a modern processor, two or more instructions can be issued per machine cycle.
A conventional processor takes one or more machine cycles to issue a single instruction. These types of processors are called one-issue machines, with a single instruction pipeline in the processor.
A multiprocessor system which built n k-issue processors should be able to handle a maximum of nk threads of instructions simultaneously

## Slide 10: Software Parallelism
It is defined by the control and data dependence of programs.
The degree of parallelism is revealed in the program flow graph.
Software parallelism is a function of algorithm, programming style, and compiler optimization.
The program flow graph displays the patterns of simultaneously executable operations.
Parallelism in a program varies during the execution period .
It limits the sustained performance of the processor.

## Slide 14: ARM processor
ARM – Advanced RISC Machine.
Family of CPU used in music players, smartphones, wearables, tablets and other electronic devices.
Very few instruction sets and transistors are needed.
Small in size – perfectly fits small devices.
Less power consumption and complexity.
Can be applied to 32-bit systems and embedded systems.

## Slide 15
Processing unit works on a set of predefined instructions – collectively called Instruction Sets.
OS and programs uses these instructions to execute themselves.
Later it was found that the many instructions were not that much used by the processor.
So, reducing the number of predefined instructions and the cutting out the hard to implement and complex instructions – RISC was formed.
This caused the processor to run faster and used less power and space on chip.

## Slide 16
X86 processor – modular approach
uses graphics card, memory control, etc.
but costly and high hardware components.

## Slide 17
In ARM processor, CPU cores are the part of the physical platform.
Other hardware functions are on the same platform.
All these are integrated through an internal bus.
This is SOC (System On a Chip)
ARM just gives a structure and the owning company can frame its own required structure around the ARM processor.