## Slide 1
Half-wave rectifier
Consider a diode rectifier:
slope=1
D
R
Vo
Vi
Vi
Vo
VD

## Slide 2: Half-wave rectifier
Consider a diode rectifier:
slope=1
D
R
Vo
Vi
Vi
Vo
VD
If Vi VD , the diode drop can be ignored.
However, if Vi is small, e.g., Vi = 0.2 sin ωt V , then the circuit does not rectify, and
Vo (t) = 0 V .

## Slide 3: Half-wave rectifier
Consider a diode rectifier:
slope=1
D
R
Vo
Vi
Vi
Vo
VD
If Vi VD , the diode drop can be ignored.
However, if Vi is small, e.g., Vi = 0.2 sin ωt V , then the circuit does not rectify, and
Vo (t) = 0 V .
Precision rectifier circuits overcome this drawback.

## Slide 4
Half-wave precision rectifier
D
R
Vi
Vo

## Slide 5: Half-wave precision rectifier
D
R
V
i
Vo
R
VD
V
i
V
o1
Vo
iR
i−
iD
Consider two cases:
(i) D is conducting: The feedback loop is closed, and the circuit looks like (except for the diode drop) the buffer we have seen earlier.

## Slide 6: Half-wave precision rectifier
D
R
V
i
Vo
R
VD
V
i
V
o1
Vo
iR
i−
iD
Consider two cases:
(i) D is conducting: The feedback loop is closed, and the circuit looks like (except for the diode drop) the buffer we have seen earlier.
Since the input current i− ≈ 0, iR = iD .
+ −
Further, V − V = =
o1 o
V V + 0.7 V
A A
V V
o i
≈ 0 V → V = V .

## Slide 7: Half-wave precision rectifier
D
R
V
i
Vo
R
VD
V
i
V
o1
Vo
iR
i−
iD
Consider two cases:
(i) D is conducting: The feedback loop is closed, and the circuit looks like (except for the diode drop) the buffer we have seen earlier.
Since the input current i− ≈ 0, iR = iD .
+ −
Further, V − V = =
o1 o
V V + 0.7 V
A A
V V
o i
≈ 0 V → V = V .
This situation arises only if iD > 0 (since the diode can only conduct in the forward direction), i.e., Vo > 0 → Vi = Vo > 0 V .

## Slide 8: Half-wave precision rectifier
D
R
V
i
Vo
R
VD
V
i
V
o1
Vo
iR
i−
iD
slope=1
Vo
Vi
Consider two cases:
(i) D is conducting: The feedback loop is closed, and the circuit looks like (except for the diode drop) the buffer we have seen earlier.
Since the input current i− ≈ 0, iR = iD .
+ −
Further, V − V = =
o1 o
V V + 0.7 V
A A
V V
o i
≈ 0 V → V = V .
This situation arises only if iD > 0 (since the diode can only conduct in the forward direction), i.e., Vo > 0 → Vi = Vo > 0 V .

## Slide 9
Half-wave precision rectifier
D
R
Vi
Vo

## Slide 10
Half-wave precision rectifier
D
R
V
i
Vo
R
V
i
Vo1
Vo
(ii) D is not conducting → Vo = 0 V .

## Slide 11: Half-wave precision rectifier
D
R
V
i
Vo
R
V
i
Vo1
Vo
(ii) D is not conducting → Vo = 0 V . What about Vo1?
Since the Op Amp is now in the open-loop configuration, a very small Vi is enough to drive it to saturation.

## Slide 12: Half-wave precision rectifier
D
R
V
i
Vo
R
V
i
Vo1
Vo
(ii) D is not conducting → Vo = 0 V . What about Vo1?
Since the Op Amp is now in the open-loop configuration, a very small Vi is enough to drive it to saturation.
Note that Case (ii) occurs when Vi < 0 V . Since V+ − V− = Vi − 0 = Vi is negative, Vo1 is driven to −V sat.

## Slide 13: Half-wave precision rectifier
D
R
V
i
Vo
R
V
i
Vo1
Vo
Vo
Vo = 0
Vi
(ii) D is not conducting → Vo = 0 V . What about Vo1?
Since the Op Amp is now in the open-loop configuration, a very small Vi is enough to drive it to saturation.
Note that Case (ii) occurs when Vi < 0 V . Since V+ − V− = Vi − 0 = Vi is negative, Vo1 is driven to −V sat.

## Slide 14: Half-wave precision rectifier
superdiode
D
2
0
−2
−4
−6
−8
−10
−12
D on
D off
1
t (ms)
2
0
Vo1
Vo R
Vi
Vo
Vo = 0
Vo = Vi
Vi
Vo
Vi
* The circuit is called a “superdiode” (i.e., a diode with zero Von).

## Slide 15: Half-wave precision rectifier
superdiode
D
2
0
−2
−4
−6
−8
−12
D on
D off
1
t (ms)
2
0
Vo1
Vo R
Vi
Vo
Vo = 0
Vo = Vi
V −10
i
Vo
Vi
−Vsat
Vo1
* The circuit is called a “superdiode” (i.e., a diode with zero Von).

## Slide 16: Half-wave precision rectifier
superdiode
D
2
0
−2
−4
−6
−8
−12
D on
D off
1
t (ms)
2
0
Vo1
Vo R
Vi
Vo
Vo = 0
Vo = Vi
V −10
i
Vo
Vi
−Vsat
Vo1
The circuit is called a “superdiode” (i.e., a diode with zero Von).
Note that the Op Amp needs to come out of saturation when Vi changes from negative to positive values. This is a relatively slow process, and it limits the speed of this circuit.

## Slide 17: Half-wave precision rectifier
superdiode
D
2
0
−2
−4
−6
−8
−12
D on
D off
1
t (ms)
2
0
Vo1
Vo R
Vi
Vo
Vo = 0
Vo = Vi
V −10
i
Vo
Vi
−Vsat
Vo1
The circuit is called a “superdiode” (i.e., a diode with zero Von).
Note that the Op Amp needs to come out of saturation when Vi changes from negative to positive values. This is a relatively slow process, and it limits the speed of this circuit.
SEQUEL file: precision half wave 1.sqproj

## Slide 18
Improved half-wave precision rectifier
iR2
iR1
iD1
R
Vo
iR
R
R2
D1
V
i 1
iD2
Vo1 D2

## Slide 19: Improved half-wave precision rectifier
iR2
iR1
iD1
R
Vo
iR
R
R2
D1
V
i 1
iD2
Vo1 D2
(i) D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .

## Slide 20: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
(i) D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .

## Slide 21: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
R
Vi > 0
Vo
R
1
D1
V
i
Vo1 D2
R2
(i) D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .

## Slide 22: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
R
Vi > 0
Vo
R
1
D1
V
i
Vo1 D2
R2
(i) D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .
iR1 = iD1 which can only be positive ⇒ Vi > 0 V .

## Slide 23: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
R
Vi > 0
Vo
R
1
D1
V
i
Vo1 D2
R2
D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .
iR1 = iD1 which can only be positive ⇒ Vi > 0 V .
D1 is off; this will happen when Vi < 0 V .

## Slide 24: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
R
Vi > 0
Vo
R
1
D1
V
i
Vo1 D2
R2
R
Vi < 0
Vo
R
1
D1
V
i
Vo1 D2
R2
D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .
iR1 = iD1 which can only be positive ⇒ Vi > 0 V .
D1 is off; this will happen when Vi < 0 V .
In this case, D2 conducts and closes the feedback loop through R2.

## Slide 25: Improved half-wave precision rectifier
iR2
iD1
R
Vo
iR
R
1
R2
D1
V
iR1
i
iD2
Vo1 D2
R
Vi > 0
Vo
R
1
D1
V
i
Vo1 D2
R2
R
Vi < 0
Vo
R
1
D1
V
i
Vo1 D2
R2
D1 conducts: V− = V+ = 0 V , Vo1 = −VD1 ≈ −0.7 V .
D2 cannot conduct (show that, if it did, KCL is not satisfied at Vo ).
→ iR2 = 0, Vo = V− = 0 V .
iR1 = iD1 which can only be positive ⇒ Vi > 0 V .
D1 is off; this will happen when Vi < 0 V .
In this case, D2 conducts and closes the feedback loop through R2.
Vo = V− + iR2R2 = 0 +
0 − V
i
R
1
„ «
R
2
R
1
2 i
R = − V .

## Slide 26
Improved half-wave precision rectifier
1 k
1 k
R
Vo
D1
Vi R1
Vo1 D2
R2
Vo
Vi
Vo = 0
R2
R1
— V
i

## Slide 27: Improved half-wave precision rectifier
1 k
1 k
R
Vo
D1
Vi R1
Vo1 D2
R2
Vo
Vo = 0
R
2
R1
— V
i
Vi
−1
2
1
0
1
t (ms)
2
0
Vo
Vi

## Slide 28: Improved half-wave precision rectifier
1 k
1 k
R
Vo
D1
Vi R1
Vo1 D2
R2
Vo
Vo = 0
R
2
R1
— V
i
Vi
−1
2
1
0
1
t (ms)
2
0
Vo
Vi
Vo1

## Slide 29: Improved half-wave precision rectifier
1 k
1 k
R
Vo
D1
Vi R1
Vo1 D2
R2
Vo
Vo = 0
R2
R1
— V
i
Vi
−1
2
1
0
1
t (ms)
2
0
Vo
Vi
Vo1
* Note that the Op Amp does not enter saturation since a feedback path is available for Vi > 0 V and Vi < 0 V .

## Slide 30: Improved half-wave precision rectifier
1 k
1 k
R
Vo
D1
Vi R1
Vo1 D2
R2
Vo
Vo = 0
R2
R1
— V
i
Vi
−1
2
1
0
1
t (ms)
2
0
Vo
Vi
Vo1
* Note that the Op Amp does not enter saturation since a feedback path is available for Vi > 0 V and Vi < 0 V .
SEQUEL file: precision half wave.sqproj

## Slide 31: Improved half-wave precision rectifier
R
V
o
R1
D2
D1
Vi
Vo1
R2
Vi
Vo = 0
Vo
R
2
R
1
— V
i
The diodes are now reversed.
M. B. Patil, IIT Bombay

## Slide 32: Improved half-wave precision rectifier
R
V
o
R1
D2
D1
Vi
Vo1
R2
Vi
Vo = 0
Vo
R
2
R
1
— V
i
The diodes are now reversed.
By considering two cases: (i) D1 on, (ii) D1 off, the Vo versus Vi relationship shown in the figure is obtained (show this).

## Slide 33: Improved half-wave precision rectifier
R
V
o
R1
D2
D1
Vi
Vo1
R2
Vi
Vo = 0
Vo
R
2
R
1
— V
i
The diodes are now reversed.
By considering two cases: (i) D1 on, (ii) D1 off, the Vo versus Vi relationship shown in the figure is obtained (show this).
SEQUEL file: precision half wave 2.sqproj

## Slide 34: AM demodulation using a peak detector
AM
signal
Super diode
filter
−0.15
0
0.15
1
t (ms)
2
0
Vo2
Vi Vo1
Vo1

## Slide 35: AM demodulation using a peak detector
AM
signal
Super diode
filter
−0.15
0
0.15
1
t (ms)
2
0
Vo2
Vi Vo1
Vo1
* charging through superdiode, discharging through resistor

## Slide 36: AM demodulation using a peak detector
AM
signal
Super diode
filter
−0.15
0
0.15
1
t (ms)
2
0
Vo2
Vi Vo1
Vo1
charging through superdiode, discharging through resistor
The time constant (RC ) needs to be carefully selected.

## Slide 37: AM demodulation using a peak detector
AM
signal
Super diode
filter
−0.15
0
0.15
1
t (ms)
2
0
Vo2
Vi Vo1
Vo1
charging through superdiode, discharging through resistor
The time constant (RC ) needs to be carefully selected.
SEQUEL file: super diode.sqproj

## Slide 38: Full-wave precision rectifier
Half−wave rectifier (inverting)
x (−1)
x (−2)
Vo1
Vi
Vi
Vo1
VB
Vi
Vi
VA
Vi
Vo
Vo
VA
VB

## Slide 39: Full-wave precision rectifier
Half−wave rectifier (inverting)
x (−1)
x (−2)
Vo1
Vi
Vi
Vo1
VB
Vi
Vi
VA
Vi
Vo
Vo
VA
VB
(SEQUEL file: precision_full_wave.sqproj)
R
R/2
R
inverting summer
inverting half−wave rectifier
Vo
R1
D1
R1
Vi
D2 Vo1

## Slide 40: Full-wave precision rectifier
Half−wave rectifier (inverting)
x (−1)
x (−2)
Vo1
V
o
Vi
Vo1
Vi
VB
Vi
VA
Vi
Vo
V
A
VB
(SEQUEL file: precision_full_wave.sqproj)
R
R/2
R
inverting summer
inverting half−wave rectifier
Vo
R1
D1
R1
Vi
D2 Vo1
−2
Vi −1
0
1
2
1
t (ms)
2
0
Vi Vo

## Slide 41
Wave shaping with diodes
D
A
R
i
R0
R′
−V0
V
0 V

## Slide 42
Wave shaping with diodes
D
A
R
i
R0
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V

## Slide 43: Wave shaping with diodes
D
A
R
i
R0
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'

## Slide 44: Wave shaping with diodes
D
A
R
i
R0
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'
R
For D to turn on, VA = Von ≈ 0.7 V → V ≡ Vbreak = R' (V0 + Von) + Von .

## Slide 45: Wave shaping with diodes
D
A
i
R0
R
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
D on
A
R
i
R′
R0
−V0
V
0 V
Von
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'
R
For D to turn on, VA = Von ≈ 0.7 V → V ≡ Vbreak = R' (V0 + Von) + Von .

## Slide 46: Wave shaping with diodes
D
A
i
R0
R
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
D on
A
R
i
R′
R0
−V0
V
0 V
Von
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'
R
For D to turn on, VA = Von ≈ 0.7 V → V ≡ Vbreak = R' (V0 + Von) + Von .
R0 R
When D is on,
V V − Von −V0 − Von i = + +
= V
R0
1 1
+
R
» –
R'
+ (constant)

## Slide 47: Wave shaping with diodes
D
A
i
R0
R
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
D on
A
R
i
R′
R0
−V0
V
0 V
Von
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'
R
For D to turn on, VA = Von ≈ 0.7 V → V ≡ Vbreak = R' (V0 + Von) + Von .
R0 R
When D is on,
V V − Von −V0 − Von i = + +
= V
1 1
+
» –
R'
+ (constant)
R0 R
i.e., V = (R0 ǁ R) i + (constant) .

## Slide 48: Wave shaping with diodes
D
A
R
i
R0
R′
−V0
V
0 V
D off
A
R
i
R′
R0
−V0
V
0 V
D on
A
R
i
R′
R
0
−V0
V
0 V
Von
i
V
Vbreak
slope = R0 ǁ R
slope = R0
When D is off, VA is (by superposition),
R'
R
VA = V − V0 .
R + R' R + R'
R
For D to turn on, VA = Von ≈ 0.7 V → V ≡ Vbreak = R' (V0 + Von) + Von .
R0 R
When D is on,
V V − Von −V0 − Von i = + +
= V
1 1
+
» –
R'
+ (constant)
R0 R
i.e., V = (R0 ǁ R) i + (constant) .

## Slide 49
Wave shaping with diodes
i
0 V
R0
V

## Slide 50
Wave shaping with diodes
i
0 V
R0
V
i
V

## Slide 51
Wave shaping with diodes
i
V
D1B
R1B
R1B′
i
−V0
0 V
R0
V

## Slide 52
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
i
V

## Slide 53
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
i
V
D2B
R2B
R2B′

## Slide 54
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
i
V

## Slide 55
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
i
V
D1A
R1A
R1A′
V0

## Slide 56
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
i
V

## Slide 57
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
i
V
D2A
R2A
R2A′

## Slide 58
Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V

## Slide 59: Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V
D1B
D2B
D2A
R1A′
R2A′
R1B
R2B
R1B′
R2B′
Vo
RL
i
R2A
R1A
i
V0
Ra
−V0
R0
Vi
Ra = 5 k R0 = 20 k
R1A = R1B = 15 k R2A = R2B = 5 k R1A′ = R1B′ = 60 k
R2A′ = R2B′ = 10 k D1A
V0 = 15 V

## Slide 60: Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V
D1B
D2B
D2A
R1A′
R2A′
R1B
R2B
R1B′
R2B′
Vo
RL
i
R2A
R1A
i
V0
Ra
−V0
R0
Vi
Ra = 5 k R0 = 20 k
R1A = R1B = 15 k R2A = R2B = 5 k R1A′ = R1B′ = 60 k
R2A′ = R2B′ = 10 k D1A
V0 = 15 V
Since Vi = −Rai , the Vo versus Vi plot is similar to the V versus i plot, except for the (−Ra ) factor.

## Slide 61: Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V
D1B
D2B
D2A
R1A′
R2A′
R1B
R2B
R1B′
R2B′
Vo
i
R2A
R1A
i
V0
Ra
−V0
R0
Vi
Ra = 5 k R0 = 20 k
R1A = R1B = 15 k R2A = R2B = 5 k R1A′ = R1B′ = 60 k
R2A′ = R2B′ = 10 k D1A
V0 = 15 V
RL −10
5
−5
−5
0
5
10
0
Vi (V)
Vo (V)
Since Vi = −Rai , the Vo versus Vi plot is similar to the V versus i plot, except for the (−Ra ) factor.

## Slide 62: Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V
D1B
D2B
D2A
R1A′
R2A′
R1B
R2B
R1B′
R2B′
Vo
i
R2A
R1A
i
V0
Ra
−V0
R0
Vi
Ra = 5 k R0 = 20 k
R1A = R1B = 15 k R2A = R2B = 5 k R1A′ = R1B′ = 60 k
R2A′ = R2B′ = 10 k D1A
V0 = 15 V
RL −10
5
−5
−5
0
5
10
0
Vi (V)
Vo (V)
2
0
6
8
10
−10
0
4
time (msec)
Vi
Vo
Since Vi = −Rai , the Vo versus Vi plot is similar to the V versus i plot, except for the (−Ra ) factor.

## Slide 63: Wave shaping with diodes
D1B
R1B
R1B′
i
−V0
0 V
R0
V
D2B
R2B
R2B′
D1A
R1A
R1A′
V0
D2A
R2A
R2A′
i
V
D1B
D2B
D2A
R1A′
R2A′
R1B
R2B
R1B′
R2B′
Vo
i
R2A
R1A
i
V0
Ra
−V0
R0
Vi
Ra = 5 k R0 = 20 k
R1A = R1B = 15 k R2A = R2B = 5 k R1A′ = R1B′ = 60 k
R2A′ = R2B′ = 10 k D1A
V0 = 15 V
RL −10
5
−5
−5
0
5
10
0
Vi (V)
Vo (V)
2
0
6
8
10
−10
0
4
time (msec)
Vi
Vo
Since Vi = −Rai , the Vo versus Vi plot is similar to the V versus i plot, except for the (−Ra ) factor. SEQUEL file: ee101 wave shaper.sqproj

## Slide 64
Wave shaping with diodes: spectrum
0
5
10
−10
0
Vi

## Slide 65: Wave shaping with diodes: spectrum
0
5
10
−10
0
Vi
2
0
6
8
10
−10
4
time (msec)
0
N
0
2
4
6
8
10
0
10
Vo